SKALLO

DIGITAL SCALE

Thank you for purchasing our pocket scale. With normal care and proper treatment, it will provide years of reliable service. Please read all operating instructions carefully before us. It may be necessary to calibrate the scale before the first use.

- Avoiding any exposure to extreme heat or cold, your scale works better when operated at normal room temperature. Always allow the scale to acclimate to normal room temperature for at least one hour before use.

- Give your scale sufficient warm up time. Usually 30-60 seconds before calibration to give the internal components a chance to stabilize.

- Keep your scale in a clear environment. Dust, dirt, moisture, vibration, air currents and a close distance to other electronic equipment can all cause an adverse effect on the reliability and accuracy of your scale.

- Handle with care. Gently apply all items to be weighed onto tray top. Although this scale is designed to be quite durable, try to avoid rough treatment as this may permanently damage the internal sensor.

- Avoid shaking, dropping or otherwise shocking the scale. This is a precision instrument and must be handled with extreme care.

- Only operate the scale on a stable, vibration free surface.

OPERATION

- Place scale on a horizontal flat surface, press ON/OFF switch

- Wait until “0.0”is displayed

- Put the object(s) on the weighing platform

COUNTING FUNCTION:

- Put the relevant amount of goods that you are going to count as the sample (25,50,75,100).

- Press and hold “pcs” key for two seconds, then you will see “100”.

- Press “MODE” key and you will see (25,50,75,100). Please select the number that you are willing to put as the sample number. Then press “pcs” key to confirm it

Now you can put the goods that you want to count on the center of the platform and the LCD will show the actual of the goods on the platform.

TARE WEIGHING

- Turn on the scale as described above

- Place the tare item on the platform

- Press TARE and wait until “0.0”(or“0.00”) is displayed

- Add the“net-weight-item”

SPECIFICATIONS

Capacity: Aries 500 : 500g , Aries 3000 : 3000g/3kg

Accuracy: 0.01g(500g)

0.1g(for 3000g)

Units: g/oz/dwt/ct

Calibration: Auto calibration

Tare range: Tare full capacity

Auto off (default): 30 seconds off

Operation temperature: 10-30℃

Display LCD 4 1/2 digits

Dimensions: 90*90*20

Weight: 125g

CALIBRATION

Standard calibration (if LCD displays “0.0” or “OUE2” after you turn on the scale):

Turn on the scale by pressing “ON/OFF”key, press “MODE”key quickly and hold it until LCD displays “CAL”. Then unit “MODE” again , after LCD flashes “CAL” and“100.0”(subject to the capacity of your scale) three times.

Add 100g (subject to the capacity of your scale) standard cal weight, wait 3-4 seconds, LCD displays “PASS”, then “100.0”. Put away calibration weight, press ON/OFF key to turn off scale, the calibration is finished.

For more information:

Skallo Corp.

P.O. BOX 656584

Fresh Meadows

11365, NY

info@skallo.nyc

www.skallo.nyc